## Slide 1
eCall and ERA-GLONASS interoperability: Work of 2017-2018
Risto Öörni, VTT
Mikko Tarkiainen, VTT
Henri Sintonen, VTT
Aleksey Golovteev, JSC GLONASS
Transport Week, Moscow, 21st November 2018

## Slide 2
Motivation
Differences between eCall and ERA GLONASS
Test objectives
Test arrangements
The first results and identified problems
The next steps
Contents
Photo: VTT
Photo: www.112.fi

## Slide 3
eCall and ERA-GLONASS
 | eCall | ERA-GLONASS
Region | EU | Russia + Belarus + Kazakhstan
Vehicle categories | M1 and N1 | All categories (M1…M3, N1…N3)
Source: https://commons.wikimedia.org/wiki/File:EU_Member_states_and_Candidate_countries_map.svg
BY
RUS
NO
Vehicles registered in ERA-GLONASS system:
2 750 797
https://aoglonass.ru/en/gais-ehra-glonass/ (cited 31.10.2018)

## Slide 4
Russian ERA GLONASS and pan-European eCall are harmonised but not identical
It is important to ensure and test system interoperability
Target is to provide service coverage for European vehicles in Russia and Russian vehicles in the EU
At the moment, there is no agreement between EU countries and Russia on handling of emergency calls from vehicles
Motivation
© OpenStreetMap contributors
2M vehicles
2M vehicles
FI / RUS
Border length 1340 km

## Slide 5
Road accidents near Finnish-Russian border
Road accidents in Finland,
< 20 km from border and involving a Russian citizen
No injuries
Accident with injuries
Fatal accident
* Fatal accidents not included in the number of injury accidents

## Slide 6
eCall system in Finland
PSAP
2G/3G
eCall IVS
MSD
Emergency response services
ERA-GLONASS system
ERA-GLONASS operator (filtering contact centre)
2G/3G
ERA-GLONASS IVS
MSD
Emergency response services
System-112 (PSAP)
MSD

## Slide 7
eCall and ERA-GLONASS Comparison (related to interoperability)
 | eCall | ERA GLONASS
GNSS | GPS + (GALILEO) | GLONASS + (GPS or GALILEO)
Emergency number | 112 | 112
MSD data transfer | In-band modem | In-band modem + SMS backup
MSD | EN15722 (version 2) | EN15722 (version 1 & version 2)
SIM card | SIM card from ? | ERA GLONASS full Mobile Virtual Network Operator SIM card
Emergency call features | Voice call, MSD (re)transmission, call back, … | Voice call, MSD (re)transmission, call back, …
Additional features | Network-based positioning, similar to other emergency calls in the EU (EN16072, Universal Service Directive) | Base for public Services and a variety of consumer Value Added Services

## Slide 8
Interoperability issue with MSD versions?
  eCall supports MSD version 2 (EN15722:2015)
  Specifications of ERA-GLONASS allow use of MSD version 1 (EN15722:2011) in IVS until January 2018
  ERA GLONASS (PSAP) supports both versions and OEMs in Russia today use MSD version 1 and only gradually may start moving to version 2
    I_HeERO (*) countries have implemented eCall in PSAPs with equipment which supports both MSD versions 1 & 2, including Finland
    => No problem with this issue!
MSD versions
Photo: www.112.fi
* I_HeERO: Harmonised eCall European Deployment, http://iheero.eu

## Slide 9
TEST OBJECTIVES: interoperability tests focused on the core features of both systems:
    Transmission, decoding and presenting of minimum set of data (MSD)
    Voice connection between user of the IVS and PSAP
    MSD retransmission
    Call back from PSAP to IVS
A specification has been created for interoperability testing
Tests in Finland and Russia have been planned and implemented in cooperation with
    Ministry of Transport of Russian Federation
    JSC GLONASS, which operates the GAIS ERA-GLONASS system
    Ministry of Transport and Communications (Finland)
    Finnish Transport Safety Agency (Trafi)
    VTT Technical Research Centre of Finland Ltd
    Emergency Response Centre Agency (Finland)
    (Supported by *I_HeERO project)
Interoperability tests of eCall and ERA-GLONASS
*I_HeERO project was funded under the Connected Europe Fund Annual Programme Grant agreement no. 1031743

## Slide 10
Qn | Interoperable features statement questions | Interop. exp. | Notes
Q1 | eCall flag, emergency call routing to PSAP |  | 
Q2 | MSD transmission to PSAP |  | (see MSD versions 1 & 2)
Q3 | MSD decoding & visualisation |  | (see MSD versions 1 & 2)
Q4 | Establish voice connection |  | 
Q5 | Call cleardown by PSAP by hanging up |  | 
Q6 | Call cleardown by PSAP by in-band modem |  | 
Q7 | Request retransmission of MSD by SMS | - | Not supported in eCall
Q8 | Request retransmission of MSD by in-band-modem |  | (SMS is used in ERA GLONASS)
Q9 | Call back from PSAP to IVS |  | Not possible if no roaming SIM
Q10 | Request retransmission of MSD (in-band modem) during call back |  | (SMS used in ERA-GLONASS), No if not roaming SIM
Q11 | Request retransmission of MSD by SMS during call back | - | Not supported in eCall
Q12 | Mobile network based positioning of the caller | - | Not in ERA GLONASS
Q13 | Mobile network provides IVS CLI to PSAP |  | Not possible if no roaming SIM
See summary of the test plan: I_HeERO M21

## Slide 11
IVS: Gemalto eCall Test Box
SIM: Elisa, Telia
Use case 1: eCall IVS in Russia contacting ERA-GLONASS system
ERA GLONASS operator (filtering contact centre)
2G/3G
eCall IVS
MSD
System-112 (PSAP)
MSD
MNOs: MTS, Megafon, VimpelCom
Points of observation
& stimulus
Use case 2: ERA-GLONASS IVS in Finland contacting eCall PSAP
PSAP
2G/3G
ERA GLONASS IVS
MSD
IVS: Fort Telecom 112 EG
SIM: JSC GLONASS
MNOs: Telia, Elisa, DNA

## Slide 12
Positive results
The MSD sent by an ERA-GLONASS IVS was successfully decoded in Finland by an eCall PSAP, this was verified for both MSD versions 1 and 2.
Successful two-way voice communication between ERA-GLONASS IVS and Finnish PSAP.
Successful transfer of MSD version 2 and two-way voice communication from eCall IVS in Russia with the Filtering Contact Center of ERA-GLONASS and the System-112 Center, using the networks of MTS and MegaFon.

## Slide 13
Work to advance interoperability is going on
Russian PSAP was not able to request a retransmission of MSD from the eCall IVS equipped with a foreign SIM card, possibly due to lack of roaming agreement in Russia
MNO VimpelCom did not route emergency calls to ERA-GLONASS system from an eCall IVS with a Finnish SIM card.
 The issue is being worked on
Call back to eCall IVS in Russia was only possible as a normal phone call (no MSD retransmission during call back).
Near the border: If the IVS is located in the territory of a foreign country, but registered to a network of its home country, the emergency call and the MSD are sent to the PSAP of the home country and emergency assistance is currently difficult
 MSD information sharing required
In Finland, the transmission of MSD from IVS equipped with foreign SIM card was successful but the presentation of the information in the PSAP was not.
  Problem identified and a fix is being tested!
Call back from an eCall PSAP to ERA-GLONASS IVS was not possible in Finland due to lack of roaming agreements.

## Slide 14
Topics for further research
  Interoperability will remain as a research topic in the future:
  NG eCall
  eCall for heavy goods vehicles
Emergency calls from vehicles in cross-border situations:
  E.g. ERA-GLONASS emergency call in territory of Finland when the IVS still connected to Russian mobile network
   (MSD) information exchange needed
Source: https://opensignal.com/

## Slide 15
ERA-GLONASS
Gateway (Russia)
Gateway (Finland)
PSAP (Finland)
MSD Database
Finnish Emergency Service
Russian base station
Russian MNO
Russian vehicle with ERA-GLONASS
A potential model for MSD information sharing between Finland and Russia
1.
2.
3.
4.
5.
6.
7.

## Slide 16
ERA-GLONASS
Gateway (Russia)
Gateway (Finland)
PSAP test environment (Finland)
MSD Database
Finnish Emergency Service
Russian MNO
Plan for the first tests of MSD information sharing between Finland and Russia
1.
2.
3.
4.
VTT SIP server

## Slide 17: Thank you!
Contact:
Risto.Oorni@vtt.fi